## Slide 1
Motor-thread
Calculates the x,y-Position of the robot
Calculates bearing (angle phi)
Drives Robot in a given direction at given Speed
(and a given distance)
IR-Proxysensor-thread
Measures Distances
Indicates direction of near Object
Stop robot if object is detected
Sound direction detection-thread
Detects direction of searched for Sound
Gives the relative direction of the Sound
Free direction detection-thread
Uses ToF-sensor
When object is encountered rotates robot to search for free space(180)
ToF-Sensor-thread
Measures distances
IR-sensor-reading-thread
Measures distances
Main-thread
Calculate travel direction(bug algorithm)
Prepare Event data to send
Send Data to computer
Decide if treasure was found
(play sound/take pictures)
Indicates if an object is detected
Gives relative direction of object
Sensor data of the 8 sensors
Give direction of travel
stops robot
Relative direction of the sound
Gives the x,y-position
Gives the bearing of the robot
gives distance data
Travel so that the object is at +- 90°.
And then in the direction of free space and sound
Gives 2 bearing and distances to the next free space.
Gives bearing of object
Rotates robot
Release the motors

## Slide 2
Sound direction detection thread functions
processAudioData:
+relativeAngle
-fills the buffer
-call fft-function
-filter out all unwanted frequencys (fanny)
-call a function to calculate phase shift between microphones
-call function to calculate the direction of the sound(maybe distance)
MicrophonePhaseShift :
-takes one complex number from the fft calculations of each microphone
-calculates the Phase between the signals of the microphone
CalculateRelativeAngle
-takes the phase from each microphone
-calculates angle from phaseshift
-(maybe distance)
getRelativeAngle (fanny):
-gets the calculated angle and gives it to the invoking function

## Slide 3: IR-Proxysensor-thread
Thread function:
-starts the IR-Sensor-reading-thread
-get data from each sensor
-calculate if object is present and the direction
-stop robot if object is detected
getObjectPresence:
-says if object is present or not
getObjectDirection(fanny):
-gives you the rough direction of the object
releaseMotors:
- Releases the robot, so it can move again.

## Slide 4
Motor-thread
Motor-thread function:
+x-position,y-position, phi-variable
-is a regulator(PI)
-init motors
-calls function to calculate Orientation
-calls function to calculate x,y position
-regulate bearing, so robot points in the desired bearing
-sets motor speed to get desired orientation
calculateBearing:
-takes motor steps
-calculates current bearing
calculateXYPosition:
-takes motorsteps
-calculates x,y-Position
isAllowedToDrive:
-lets functions enable or disable forward driving
setDesiredBearing(fanny):
-lets functions set the desiredBearing
getXPosition(fanny):
-gives x-Position of robot
getYPosition(fanny)::
-gives y-Position of robot
getBearing(fanny):
-gives bearing(phi) of robot